Threaded Rod
Fig 1: Nut placement on the M5 Threaded rod
1) Thread an M5 nut up about 1 cm on the 5mm threaded rod. (Figure 1)

Fig 2: Washer placed on the nut

2) Slide an M5 washer onto the side of the nut with the longer amount of exposed threaded rod. (Figure 2)

Fig 3: Coupling placement

3) Slide the coupling onto the threaded rod up to the nut.
(Figure 3)

Fig 4: Tightening the Set Screws
4) Tighten the two set screws on the coupling covering the threaded rod. (Figure 4)

5) Slide the 625zz Bearing over the threaded rod. (Figure 5)
Fig 5: 625zz Bearing on the threaded rod
Fig 6: Placing the coupling on the motor shaft
Fig 7: Tightening the coupling set screws
Fig 8: Motor placement in carriage

6) Slide the open end of the coupling over the motor shaft. Be sure to line up one of the set screws with the flat on the motor. (Figure 6)

7) Tighten the two set screws on the coupling. (Figure 7)

8) Insert the motor/threaded rod combo into the carriage such that the motor wires come out of the side opposite of the opening. (Figures 8 & 9)

Fig 9: Motor position in carriage.

Fig 11: Placement of the M2.5 Screws

9) Put the carriage/motor/threaded rod assembly onto the motor assembly. Make sure that the open side of the carriage is on the same side as the syringe holder. Place 4 M2.5 x 10 mm into the motor screw holes. (Figures 10 & 11)

Fig 10: Position of the motor carriage

Fig 12: Tightening the M2.5 screws

10) Using a 2 mm Alan wrench, completely tighten the 4 M2.5 screws. (Figure 12)
11) Push the 625zz bearing completely into the bearing slot. (Figure 13)
Fig 13: Pushing the bearing into the housing

Fig 14: Tightening the M5 nut up to the bearing

12) Tighten the M5 nut against the bearing. (Figure 14)

13) Slightly loosen the coupling set screws and push the coupling up against the nut. Tighten the set screws. (Figure 15)
Fig 15: Moving the coupling up to the nut