Carriage
Fig 1: Inserting Guide Rod

1) Push the 6mm smooth rod into the rod clamps. (Figures 1 & 2) DO NOT POUND THE ROD INTO THE HOLE. It should slide in with only a small amount of force. Repeat with the second rod (Figure 3)
Fig 2: Guide rod fully inserted

Fig 3: Both Guide rods installed

2) Slide an M5 nut into the nut trap in the carriage. (Figure 4 &5)
Fig 4: Nut being inserted into carriage nut trap
Fig 5: Nut fully inserted into nut trap
Fig 6: Bearing being pushed into retainer
Fig 7: Bearing fully inserted

3) Next, pop an LM6UU linear bearing into one of the bearing retainers on the carriage. (Figure 6) It may take some force to get it into the retainer, but should sit fully inside. (Figure 7)
4) Repeat step 3 with the other LM6UU. (Figure 8)
Fig 8: Both bearings fully inserted
Fig 9: Inserting Zip Tie
Fig 10: Zip tie being tightened
Fig 11: Fully tightening the Zip Tie

5) Next, insert a small zip tie into the hole besides the bearing. It should slide all the way through and out the adjacent hole. (Figure 9)

6) Slide the zip tie tight around the bearing. Needle nose pliers may be necessary to tighten the zip tie fully. (Figures 10 & 11) Cut off the excess zip tie. (Figure 12)

Fig 12: Bearings inserted with zip ties tightened and excess cut off.

7) Finally, slide the carriage onto the smooth and threaded rod. Make sure the syringe pusher is on the same side as the syringe holder. (Figure 13) Thread the threaded rod through the M5 nut until the smooth rod can be seen just over the top the bearings. (Figure 14)
Fig 13: Placing the carriage on the guide rods and threaded rod.
Fig 14: Carriage correctly installed on guide rods